## Slide 1
A PPT on Equipment in C.N.S Department

## Slide 2: COMMUNICATION
The communication department in Airport Authority of India deals with all type of communications that takes place in airport:
1.Ground to Air
2. Ground to Ground
The ground to air communication is the exchange of information between Pilots and the ATC people.
Where as the ground to ground communication is between one airport and other airport, within the airport etc.They use Walkie-Talkies,Telephones,Hotlines(dedicated lines) and AMSS(Automatic Message Switching System) for this purpose.

## Slide 3: GROUND TO AIR
We use VHF(Very high Frequency) band for communication between ATC and Aircrafts.
The range of frequencies in VHF is 30M to 300M Hz. In this range the aeronautical band is 117.975M to 136.975M Hz.
The drawback of VHF range is that LINE OF SIGHT.
We also use HF(high frequency) band but in oceanic aspects only
The drawback of HF range is that NOISE.

## Slide 4: EQUIPMENT
The main equipment used in communication department are
1. VHF Transmitters and Receivers.
2. VCCS( Voice Communication Controlled Switching).
3. DATIS( Digital Airport Terminal Information System).

## Slide 5: VHF Tx AND Rx
We us the OTE make VHF transmitters and receivers
We use 2 frequencies in Gannavaram Airport :
Main: 118.55MHZ
Alternate: 118.65MHZ
The purpose for using 2 frequencies because in emergency case if the main one fails then the alternate one can be used.
Main module of Transmitter consists of:
1.Transmitter Module
2.Baseband Module
3.Power Supply Unit

## Slide 6
The VHF receiver used here is the Super Heterodyne Receiver.
It consists of Limitter ,Attenuator , Low power amplifier, Mixer etc.
This type of receivers offers high sensitivity and selectivity.
We have 2 Transmitters for main frequency and also for alternate frequency.
We use 2 txs because one can be used as stand by if other one fails.
Similarly the receivers are also 2 in number for each frequency.

## Slide 7: VCCS
VCCS stands for Voice Communication Controlled Switching.
Its make is Schmid.
VCCS purpose: It controls and connects together various voice communication systems used in Airport sucs as VHF Tx and Rx , Telephone, Hotline etc.
It has 200 operator positions.
It has 60 time slots : 59 are digital and 1 is analog.
There are 3 main subsystems in VCCs:
1.Server System, 2. Interface System, 3.Operator Position Rings.

## Slide 8: DATIS
DATIS stands for Digital Airport Terminal Information System.
It provides the pilot in aircraft information about the airport terminal.
The frequency allotted for DATIS in Gannavaram is 128.4MHZ.
It tells the pilot about the Wind speed and direction, Any bird activity, temperature , pressure and weather.
The information to DATIS is provided by the METEROLOGICAL department that is presented at the airport.

## Slide 9: NAVIGATION
The Navigation department provides navigational or the routing aid for an Aircraft.
This is done by the equipment:
1. DVOR & DME
2. NDB
3. ILS

## Slide 10: DVOR
DVOR stands for Doppler VHF Omni Range
It provides Magnetic bearing for the Aircrafts
Magnetic bearing gives angle between nose of the aircraft and Magnetic North.
Its range is 108MHZ to 118MHZ.
The antenna used in DVOR is Alford Loop Antenna.It consists of49 side antennas and one center antenna.
The modulation technique used in DVOR is SPACE MODULATION.
DVOR is a high power device

## Slide 11: DME
DME stands for distance measuring equipment.
It gives the slant distance between aircraft and the airport.
Since it is working along with the DVOR it is also a High Power Device.
Its principle is reverse to that of a Secondary RADAR.
The antenna used in DME is Biconical Antenna.
Its range of frequency us 916MHZ to 1213MHZ.

## Slide 12: NDB
The word NDB stands for Non Directional Beacon.
Purpose: It gives the Relative bearing
Relative Bearing is the angle between nose of the aircraft and the airport.
Its make is SAC500.
Its range is 190KHz to 1750KHZ here we use 393KHZ.
It consists of Automatic direction Finder. It uses Vertically Polarised and ground wave propagation.
We use T-Cage antenna here.
DVOR is replacement for NDB , but still we use NDB as some of the
old aircrafts didn’t have equipment matches to DVOR and also as a alternate to DVOR in emergency cases.

## Slide 13: ILS
ILS is Instrument Landing System.
It consists of 2 components:
1.Localiser
2.Glide Path.
Localiser provides Azimuthal guidance i.e as Aircraft approaches for landing it provides information about whether the aircraft is aligned to center line or not. Its frequency range is 108MHZ to 112MHZ.
Glidepath provides the Vertical Guidance i.e it gives the approach angle which is 3 degrees for perfect landing. It uses Difference in depth of modulation and Sum in depth of modulation technique.Its frequency range is 328MHZ to336MHZ.

## Slide 14: SURVEILLANCE
The surveillance in the CNS department gives the whereabouts of the aircraft.
RADAR is used in surveillance in some airports and some airports uses ADSB.
In Gannavaram airport ADSB is used.

## Slide 15: RADAR
RADAR stands for Radio Detection and Ranging.
There are 2 types of RADARs: Primary and Secondary.
RADAR emits radio signals in air and whenever it touches an obstacle the signal return backs and the distance is measured.
In primary RADAR signal power is reduced so we use secondary RADAR.
In secondary radar ATC and aircraft both have transponder.
If radar system is not responding or it is unavailable in that region then the ADSB is used.

## Slide 16: ADSB
ADSB stands for Automatic Dependent Surveillance Broadcast.
It uses GPS and it is a satellite based system.
It consists of 2 sensors A & B. They take the information from the GNS satellites and passes it to the ADSB servers where automation system is present.
The Automation System correlates the Flight Plan Data which is received from AMSS and the surveillance data received from the sensors and provides the location of the aircraft.
It consists of Automation Servers and Control Systems.

## Slide 17: SERVERS
1.RDCU- Radar Data Control Unit: It converts 3d data into 2d data.It consists of 3 data formats DF17 used in Civil Aviation,DF18 used in Site monitoring,DF19 used in Military.
2.SDP-Surveillance Data Processor: It correlates Surveillance data and FDP.
3.FDP-Flight Data Processor: It created flight plan , edit it , delete it etc.
4.SNET-Safety Net: IT ensures safety , it adds safety. It is the inbuilt feature of SDP.
5.DRF-Data Recording Facility: Records all Data.
6.Neptuno:Voice recorder.
7.NTP-Network Time Protocol: It syncs time in all servers.
8.DBM-Data base Management: Design shapes etc.

## Slide 18: CONTROL SYSTEMS
SDD-Situation data display: It displays the surveillance data.
FDD-Flight data display.
CMD-Control & Monitoring Display: It gives the status of all Servers and Control Systems. Colour coding is present:
Red-Shutdown
Orange-Software Shutdown
Green- Working
Blue-Replaying.
Nep- Sup: Neptuno Supervisor , controls the neptuno server.

## Slide 19: SECURITY IN AIRPORTS
X-RAY BIS: It is a baggage inspection system. The luggage of passengers are placed on the conveyer belt of the machine. It sends the x-rays which are collected by the receivers at the other end. They displays different colours for different type of materials like
Organic-Orange
Inorganic-Green
Metal-Blue.
DFMD-Door Frame Metal Detector: It detects the metal objects whenever a person passes through it. It uses PULSE INDUCTION technology.

## Slide 20
HHMD-Hand Held Metal Detectors: Its working is similar to that of DFMD but here it is operated by a person.
ETD-Explosive Trace Detectors: Blastic explosives and Narcotics are cant be detected by X-RAY BIS so we use ETD. The sample is taken with a card jus a small swipe over the object and the ETD heats the sample to an extent of 1000 degree centigrade at that temperature they emit gases so the narcotics can be detected.
CCTV-Closed Circuit Television: Through CCTV all the parts of the airport can be seen.
PA System-Public Addressing System: Through this system passengers can be intimated about flight timings etc.

## Slide 21
FIDS-Flight Information Display System: It displays the flight schedule.
DAS-Distributed Antenna System: Antennas are placed all over the airport so that mobile signals have adequate strength.

## Slide 22: DEVICE PROTETCTION
Un-Interrupted Power Supply(UPS): UPS gives power supply to the equipment when the actual power supply goes off.
It consists of a rectifier , inverter , battery , static bypass.
Rectifier converts AC supply to DC to enabling the battery to store.
If in case the inverter fails then raw AC supply goes to load by static bypass.
If AC ip is absent battery is used. Deep Discharging Protection is present in UPS which stops battery discharge after 80%.

## Slide 23
EARTHING:
In circuits leakage current is present , they are harmful to humans and devices So for discharging this false current Earthing is used . It grounds this current.
There are 2 types of earthing:
1.Conventional Earthing.
2.Chemical Earthing.
No maintainence is required for chemical but needed for conventional.But conventional is preferred as its cause no harm to the Earth.

## Slide 24
LIGHTNING ARRESTER: It grounds the lightning current as they cause damage to the equipment.
It consists of Air-terminal , Down conductor, Earthing.
Lightning is a Negative electric field and Earthing is a Positive electric field so the lightning is attracted by the Earthing.
They are 2 types- Conventional and Advanced Lightning arrester.

## Slide 25: THANK YOU